## Slide 1
Motherboard & It’s Components

## Slide 3
Main circuit board which is directly / indirectly connected to each part of PC
Made up of chipsets
Different types of motherboard are consists of more and complex buses and extra parts which differs in the rate
Most commonly found parts on the motherboard are : CPU Chip, Co-Processor Chip, Memory Chips, Expansion Slots, Buses, System Clock, ROM Bios, Battery, Ports, NIC, SMPS etc.

## Slide 4
CPU Chip
Main component of motherboard
Varies from PC to PC according to models
It processes the data and controls the function of PC

## Slide 5
Co-Processor Chip
Helps the CPU chip
There are various Co-Processor chips like math co-processor chip, logical co-processor chip

## Slide 6
Memory Chips
Physically installed on the motherboard by 3 different methods.
DIP: Dual Inline Packaging Method
SIMM: Single Inline Memory Module Package
SIPP: Single Inline Pin Package

## Slide 7
Expansion Slots
Connectors on the motherboard which allow us to connect extra cards like: sound card, graphics card, hard disk.

## Slide 8
Buses
Different colored lines plotted on the motherboard which moves the information from one part of computer to the other part of computer.
3 Types of bus are: Data Bus, Address Bus, Control Bus

## Slide 9
System Clock
Used to synchronize the activities of the various components of computer.
ROM BIOS
Stores the System Programs which performs supervisory and support tasks in computer.
Battery
Used to power clock and BIOS.

## Slide 10
Ports
Used to connect devices to the Computer.

## Slide 11
NIC
Network Interface Card.
Allows the computer to connect to the Network

## Slide 12
SMPS
Switched Mode Power Supply
An electronic Power supply unit which works as switching regulator.
It turns the load current ON and OFF to the internal parts to stabilize the output voltage

## Slide 13
The C.P.U.

## Slide 14
An IC chip with different circuits to perform arithmetic al , logical and controlling function
Located on the motherboard
Speed measured in the terms of Mega Hertz or Giga Hertz
ALU: Performs arithmetical and logical operations
CU: Generates the signals necessary for execution of instruction and also controls the flow of information among processor and peripherals.
Registers: used to store the data temporary by processor also manipulates the data and instruction. Most commonly used registers are : PC, MAR, MBR, IR, AX 4

## Slide 15
Types of Registers used in C.P.U.
PC (Program Counter) : a register which hold the address of the instruction which will be executed next.
MAR (Memory Address Register) : It contains the address of current instruction. Connected to the address lines of the system.
MBR (Memory Buffer Register) : It is connected to the address lines of the system and works as the interface among the C.P.U. and Memory. On receiving the signal from C.U. , the memory location stored in the memory address register is used to copy data from or to the memory buffer register.

## Slide 16
Types of Registers used in C.P.U. (cont.)
IR (Instruction Register) : Holds the instruction till it id decoded.
AX (Accumulator) : Stores the result generated by the A.L.U. temporary.

## Slide 17
The functioning of the C.P.U. Based on architectures upon which its designed
some architectures are: CISC and RISC
CISC (Complex Instruction Set Computer)
Large instruction set with variable length instruction
Variety of addressing modes
Used in the Personal Computer
RISC (Reduced Instruction Set Computer)
Small Instruction Set with fixed length instruction
mostly used in workstations

## Slide 18
PORTS

## Slide 19
An interface to connect I/O devices to computer
mouse, keyboard, printers, speakers, monitor are connected to computer via different ports
basic types of ports are: Serial Port, Parallel port, USB Port

## Slide 20
Serial Port
Serializes the data
If 1byte of instruction is sent via serial port it transmits 1 bit at a time.
With each transmit it sends a start bit ahead of actual data as 0 which also termed as parity bit.
Known as COM ports also.
It works in bi-directional way with having different pins for receiving and transmission.
For transmission of 8 bits it requires one wire (sends bit one by one).
Bit slower.

## Slide 21
Parallel Port
Faster than serial port
Sends the data simultaneously on 8 parallel connected wires
SPP (Standard Parallel Port )
EPP (Extended Parallel Port)
ECP (Extended Capability Port)

## Slide 22
USB Port
Mostly found in today’s computers as separate USB cards with no of slots on it.
mouse, keyboard, printers, pen drives, speakers, webcams, joysticks, mobile connectors, etc.
basic two type of USB connectors are there: “A” and “B”
“A” has upstream head towards computer
“B” has downstream head towards the individual device connected to computer

## Slide 23
What is UART?
one kind of controller chip
Universal Asynchronous Receiver/Transmitter
Serial ports rely on it for working properly
It takes parallel output from system bus and converts it to sirial form to transmit over serial port.

## Slide 24
Instruction

## Slide 25
A command given to the computer to perform specific action on the specific data.
consists of two parts: op-code and operand
OP-Code: Specifies the action to be taken on the mentioned data by the computer
Operand: Specifies the data which will be operated by the computer with certain op-code
Instruction may be of multiple bytes: where first byte is the op-code where as others are operands.
Types of instruction: one word or 1 byte instruction, two word or 2 byte instruction, three word or 3 byte instruction.

## Slide 26
One word or 1 byte Instruction
Instruction is of 1 byte only which may consists of only op-code or op-code and operand both.
Move A, B
Add B
RAL
Move C

## Slide 28
Two word or 2 byte Instruction
1st byte of instruction is op-code where as the 2nd byte is the operand or the address of data
Stored on the consecutive memory locations
Move B, 05 (1st byte – Move B, 2nd byte – 05)

## Slide 30
Three word or 3 byte Instruction
1st byte of instruction is op-code where as the 2nd and 3rd byte is the operand or the address of data of 16 bit
Stored on the 3 consecutive memory locations
STA 2030H (data stored on the 2030H address will be moved to the accumulator)

## Slide 32
Instruction Cycle

## Slide 33
The necessary steps performed by CPU to fetch an instruction and data from Memory and execute it are known as Instruction Cycle
Composed of Fetch Cycle and Execute Cycle
The Diagram is as follows:
IC = FC + EC
(Instruction Cycle) (Fetch Cycle) (Execute Cycle)
Start
Fetch Next
Instruction
Execute Instruction
Halt
Fetch Cycle
Execute Cycle

## Slide 34
It can also depict in following four steps:
Fetch the Instruction
  PC stores the address of Instruction to be executed
  Data bus fetches the data from above mentioned address from MAR and moves it to MBR then the MBR sends it to IR via Data bus for decoding the instruction to machine language
  Increments the PC counter
Decode the Instruction
  The decoder program stored in memory decodes the instruction at IR
  The decoded instruction stored in general purpose register
Execute the Instruction
  The control unit sends the decoded instruction to proper part of CPU for execution
Store the Result
  The result is delivered to main memory or output device

## Slide 35
Fetch Cycle
  Necessary steps taken to fetch an instruction from memory constitutes Fetch Cycle
  The time for fetching an instruction is fixed
  PC holds the next instruction to be executed which is transferred to the MAR
  PC => MAR
  The Instruction received on the MAR are transferred to MBR via data bus
  MAR=>Memory(Data Bus)=>MBR
  This cycle ends with the transfer from MBR to IR as well as incrementing the PC
  MBR => IR
  PC => PC + 1

## Slide 36
Execute Cycle
  Necessary steps taken to get data if any in memory and to perform specific operation mentioned in the instruction; constitutes an execute cycle
  The time to execute decoded instruction is varied instruction by instruction as per the type of instruction
  There is a decode program, which decodes the instruction located on the IR
  IR => decode circuitry
  If the operand mentioned in decoded instruction is available in the general purpose register then the execution performed immediately otherwise CU performs necessary actions to relocate the instruction on other register
  If operand is in general purpose register
  Executes instruction
  Else
  CU relocates the instruction
  and Executes the instruction

## Slide 37
Clock Cycle
  The time interval between two consecutive clock pulses of system clock
Wait Cycle
  The clock cycle for which CPU waits
  It depend on the memory as well as the instruction
Machine Cycle
  The necessary steps carried out to perform operation of accessing memory or any I/o devices constitutes a machine cycle
  The necessary steps carried out to perform fetch, read or write operation constitutes a machine cycle